ESP32
HTTP
Microcontroller
Web Interface
IoT PROJECT
Automatic
Plant Watering
System
5V DC
ADC
Relay Control
Soil Sensing
ESP32 · Relay · Web Server

---
What Is It?
A smart IoT system that monitors soil moisture and controls a water pump automatically
Soil
Sensor
ESP32
Water
Pump
▶
▶
Reads moisture
levels via ADC
Processes data
& controls relay
Activated when
soil is dry
No manual watering needed — the system decides when and how much to water

---
Hardware Components
ESP32 Dev Board
5V Relay Module
Soil Moisture Sensor
Dual-core 240 MHz · Built-in WiFi
& Bluetooth · 12-bit ADC · GPIO pins
Electrically isolates pump circuit
From ESP32 · Handles AC or DC loads
Resistive probe · Analog output
Connects to GPIO 32 · 3.3V powered
Mini Water Pump
Power Supply
WiFi Network
Submersible DC pump · 3–6V · Low
power · Sits in water reservoir
5V USB adapter for ESP32
Separate supply for pump if needed
ESP32 connects to local WiFi
Dashboard accessible from any browser

---
How It Works
Sense
1
Soil moisture sensor reads analog voltage — dry soil = high ADC value (>2000)
Process
2
ESP32 reads ADC on GPIO 32, converts raw value to moisture percentage (0–100%)
Decide
3
If moisture < threshold (ADC > 2000), esp32 ‘s control pin become HIGH and
Water
4
Water pump runs until moisture rises above threshold, then relay turns OFF
Report
5
Web server serves live dashboard at ESP32's IP — view moisture % and pump state

---
Web Server & Dashboard
API Endpoints
WiFi Connected
ESP32 joins your local network on boot
/
Full HTML dashboard
Built-in Server
/data
WebServer library on port 80 — no extra hardware
Live Dashboard
Sample /data response:
Moisture %, pump state, ADC gauge — auto-reloads every 1s
Any Device
Open in browser on phone, tablet, or PC on same WiFi
JSON Endpoint

---
Applications & Uses
Home Garden
Seedling Nursery
Keep indoor or balcony plants watered automatically while away on holiday
Maintain optimal moisture for seedlings that need consistent care
Greenhouse
Remote Monitoring
Scale to multiple sensors and pumps for professional greenhouse management
Check plant health from anywhere on your phone via the web dashboard
Data Logging
Smart Home
Extend /data endpoint to log history — track plant health over time
Integrate with Home Assistant, MQTT for full smart home control

---
Features & Advantages
12-bit
1s
₹
ADC Resolution
Refresh Rate
Component Cost
4096 levels of precision — accurately detects subtle moisture changes
Dashboard auto-reloads every second — truly real-time monitoring
Affordable hardware — ESP32 + sensor + relay is a low-budget build
WiFi
24/7
JSON
Connectivity
Autonomous
Open API
No extra hub or gateway needed — ESP32 connects directly to your router
Runs continuously without human intervention — fully automated
Extend to any app, dashboard, or home automation platform easily

---
Automatic Plant
Watering System
ESP32 · Relay Module · Soil Sensor · Web Dashboard
WiFi Enabled
Auto Control
Live Dashboard
Open API
Expandable